CISP440

Joseph Morgan

Homework 2
Number Line of All Possible Values

Floating Point Addition Output

This output was piped directly from my running program into a text file.
This was done via:
$: cat ./input.txt | ./test_software_float.out > output.txt
I've removed superfluous output lines.

**** Joseph Morgan's test main for software implementation of floats ****

* * * * * * * * * * * * * * * * *

First Number: 3.14159
Second Number: 2.75
#1 Expanded: 0000001100100000
#2 Expanded: 0000001011000000
Sum: 0000010111100000
Sum Normalized: 0000000010111100
Sum Packed: 00111110

* * * * * * * * * * * * * * * * *

Sum: 05.75000000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: -4.6
Second Number: 1.92
#1 Expanded: 0000010010000000
#2 Expanded: 0000000111100000
Sum: 0000001010100000
Sum Normalized: 0000000010101000
Sum Packed: 10101101

* * * * * * * * * * * * * * * * *

Sum: -02.62500000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: 2.125
Second Number: -7.79
#1 Expanded: 0000001000100000
#2 Expanded: 0000011111000000
Sum: 0000010110100000
Sum Normalized: 0000000010110100
Sum Packed: 10110110

* * * * * * * * * * * * * * * * *

Sum: -05.50000000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: -0.4887
Second Number: -13.8
#1 Expanded: 0000000001111100
#2 Expanded: 0000110110000000
Sum: 0000110111111100
Sum Normalized: 0000000011011111
Sum Packed: 11011111

* * * * * * * * * * * * * * * * *

Sum: -13.50000000

* * * * * * * * * * * * * * * * *
Floating Point Multiplication Output

**** Joseph Morgan's test main for software implementation of floats ****

Please enter a number to use in the test:
Menu options:

     1 - test atof
     2 - test ftoa
     3 - test add
     4 - test multiply
     5 - input new number
     0 - exit

Selection:
What would you like to multiply with your number?
Please enter a number to use in the test:

* * * * * * * * * * * * * * * * *

First Number: 2.7
Second Number: 1.5
#1 Expanded: 0000 0001 0101 0000
#1 Exponent: 1
#2 Expanded: 0000 0001 1000 0000
#2 Exponent: 0
Product: 0000 0001 1111 1000
Product Exponent: 1
Pruduct Packed: 0111 1101

* * * * * * * * * * * * * * * * *

Sum: 03.87500000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: -1.0
Second Number: 2.5
#1 Expanded: 0000 0001 0000 0000
#1 Exponent: 0
#2 Expanded: 0000 0001 0100 0000
#2 Exponent: 1
Product: 0000 0001 0100 0000
Product Exponent: 1
Pruduct Packed: 1010 0101

* * * * * * * * * * * * * * * * *

Sum: -02.50000000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: 3.75
Second Number: -.225
#1 Expanded: 0000 0001 1110 0000
#1 Exponent: 1
#2 Expanded: 0000 0001 1100 0000
#2 Exponent: -3
Product: 0000 0011 0100 1000
Product Exponent: -1
Pruduct Packed: 1101 0011

* * * * * * * * * * * * * * * * *

Sum: -00.81250000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: -6.333
Second Number: -2.1
#1 Expanded: 0000 0001 1001 0000
#1 Exponent: 2
#2 Expanded: 0000 0001 0000 0000
#2 Exponent: 1
Product: 0000 0001 1001 0000
Product Exponent: 3
Pruduct Packed: 0100 1111

* * * * * * * * * * * * * * * * *

Sum: 12.50000000

* * * * * * * * * * * * * * * * *

* * * * * * * * * * * * * * * * *

First Number: -6.333
Second Number: -2.1
#1 Expanded: 0000 0001 1001 0000
#1 Exponent: 2
#2 Expanded: 0000 0001 0000 0000
#2 Exponent: 1
Product: 0000 0001 1001 0000
Product Exponent: 3
Pruduct Packed: 0100 1111

* * * * * * * * * * * * * * * * *

Sum: 12.50000000

* * * * * * * * * * * * * * * * *
Source Code

main and helper functions

#include <cstdio>
#include "./float_software.h"

void get_number(char*);
void test_atof(char*);
void test_ftoa(char*);
void test_add(char*);
void test_multiply(char*);

const int INPUT_BUFFER_SIZE = 40;

int main() {
char user_input[INPUT_BUFFER_SIZE];
int selection;
bool exit = false;
char trash;

printf(
"\n\n**** Joseph Morgan's test main for software implementation of floats ****\n\n"
);
get_number(user_input);

while (!exit) {
printf(
"Menu options:\n\n"
" 1 - test atof\n"
" 2 - test ftoa\n"
" 3 - test add\n"
" 4 - test multiply\n"
" 5 - input new number\n"
" 0 - exit\n\n"
"Selection: "
);

while ((trash = getchar()) != '\n' && trash != EOF)
/* discard */;

scanf("%i", &selection);
printf("\n");
switch (selection) {
case 0 :
exit = true;
break;

case 1 :
test_atof(user_input);
break;

case 2 :
test_ftoa(user_input);
break;

case 3 :
test_add(user_input);
break;

case 4 :
test_multiply(user_input);
break;

case 5 :
get_number(user_input);
break;

default :
printf("That didn't seem like an acceptable option\n");
}
}
}

void get_number(char* user_input) {
printf("Please enter a number to use in the test: ");
scanf("%s", user_input);
printf("\n");
}

void test_atof(char* user_input) {
unsigned char f = software_atof(user_input);

printf("Converting %s to floating-point format...\n\n", user_input);

printf("* * * * * * * * * * * * * * * * *\n\n");
print8bits(f);
printf("\n* * * * * * * * * * * * * * * * *\n\n");
}

void test_ftoa(char* user_input) {
printf(
"This will show the exact value of your number as it's stored in memory in floating point format\n"
"You can see how accurately your number is being represented in 8 bits!\n\n"
"Converting %s to floating-point and back to a string...\n\n", user_input
);

unsigned char f = software_atof(user_input);
char buffer[INPUT_BUFFER_SIZE];
software_ftoa(f, buffer);

printf("* * * * * * * * * * * * * * * * *\n\n");
printf("%s\n\n", buffer);
printf("* * * * * * * * * * * * * * * * *\n\n");
}

void test_add(char* user_input) {
char second_input[INPUT_BUFFER_SIZE];
unsigned char first_number;
unsigned char second_number;
unsigned char sum;
char str_sum[INPUT_BUFFER_SIZE];;

printf("What would you like to add to your number?\n");
get_number(second_input);

printf("\n"
"* * * * * * * * * * * * * * * * *\n\n");
first_number = software_atof(user_input);
second_number = software_atof(second_input);

printf("First Number: %s\n", user_input);
printf("Second Number: %s\n", second_input);

sum = software_float_add(first_number, second_number);
software_ftoa(sum, str_sum);

printf("\n* * * * * * * * * * * * * * * * *\n\n");
printf("Sum: %s\n\n", str_sum);
printf("* * * * * * * * * * * * * * * * *\n\n");
}

void test_multiply(char* user_input) {
// TODO
printf("User input: %s", user_input);
}

Implementation

#include <stdio.h>
#include <string.h>
#include <stdlib.h>
#include "float_software.h"

unsigned char software_atof (char* input_str) {
char formatted_str[20];
bool negative = false;

// Set negative flag
if (input_str[0] == '-') {
negative = true;
strcpy(formatted_str, input_str + 1);
} else {
strcpy(formatted_str, input_str);
}

int len = strlen(formatted_str);

// Variables to hold string representation of whole and fractional parts
// of the number.
#	define S_WHOLE_SIZE 3
#	define S_FRACT_SIZE 9
char string_whole[S_WHOLE_SIZE] = "00";
char string_fract[S_FRACT_SIZE] = "00000000";

// Store the index of the decimal in x
int x = 0;
while (formatted_str[x] != '.') {
++x;
if (x > len) printf("You need to include a decimal point - exiting\n"), exit(1);
}

// Reverse whole part of number, store as string.
// ex. 3.1416 would be stored as: 30
for (int i = x - 1, j = 0; i >= 0; --i, ++j) {
string_whole[j] = formatted_str[i];
}

// Reverse fractional part of number, store as string.
// ex: 3.1416 would be stored as: 00006141
for (int i = x + 1, j = S_FRACT_SIZE - 2; i < len; ++i, --j) {
string_fract[j] = formatted_str[i];
}

// Convert string representation of whole part to internal representation of
// the integer.
unsigned char integer_whole = 0;
for (int i = 0; i < S_WHOLE_SIZE - 1; ++i) {
integer_whole += (string_whole[i] - '0') * software_float_pow(10, i);
}

// Convert string representation of fractional part to binary representation
// of the number times 100,000,000 in decimal
unsigned long integer_fract = 0;
for (int i = 0; i < S_FRACT_SIZE - 1; ++i) {
integer_fract += (string_fract[i] - '0') * software_float_pow(10, i);
}

// This is some wacky voodoo magic. To manually find the bits needed to
// represent the fractional point of a decimal number, we subtract by known
// powers of two if the fractional part is greater than the known power of two.
// Our integer_fract contains (fractional part of the integer * 1,000,000), which
// means we can subtract by (known powers of two * 1,000,000) to find which
// known powers of two it contains. Then mask off those specific bits.
unsigned long power_of_two = 50000000;
unsigned char binary_fract = 0; // Bits to the right of decimal point.
unsigned char mask = 0x80; // initial bit to potentially mask.

for (int i = 0; i < S_FRACT_SIZE - 1; ++i) {
if (integer_fract >= power_of_two) {
binary_fract |= mask;
integer_fract -= power_of_two;
}

mask >>= 1;
power_of_two >>= 1; // This is the same as multiplying by .5, ignoring remainder
}

//print8bits(integer_whole);
//print8bits(binary_fract);

unsigned short buffer = 0;
buffer = integer_whole;
buffer <<= 8;
buffer |= binary_fract;

//print16bits(buffer);

// Normalize the fraction - find the first 1.
int exponent = 7;
unsigned short bitfinder_mask = 0x8000;
while (!(buffer & bitfinder_mask)) {
--exponent;
bitfinder_mask >>= 1;
}

// Final packing of the float
unsigned char the_float = 0;

buffer <<= (7 - exponent);
buffer >>= 8;
the_float = buffer;
the_float &= 0x78;
exponent += 4;
the_float |= exponent;
if (negative) the_float |= 0x80;

return the_float;
}

void software_ftoa (unsigned char f, char* strOut) {
// This function copy/pasted from assignment
int ch_p = 0;	// pointer to string chars

if(f & 0x80) strOut[ch_p++] = '-';	// is it negative

int exponent;
exponent = (f & 0x07) - 4;	// get the exponent
f &= 0x78;	// mask off everything except mantissa
f |= 0x80;	// put on the leading 1

//print8bits(f);

// now pack the normalized bits to a 'bit field' so
// so we can de-normalize it
unsigned short buffer = 0;
buffer = f;
buffer <<= 8;	// scoot into high byte
buffer >>= (7 - exponent);	// de-normalize

//print16bits(buffer);

// get the whole part
unsigned char i_whole;	// bits to left of decimal
i_whole = (buffer & 0xFF00) >> 8;

// get the fractional part
unsigned char b_fract;	// bits to right of decimal
b_fract = (buffer & 0x00FF);

// add up the bit values in the mantissa using INTEGERS only
// we are adding up negative powers of 2 scaled by 100,000,000 decimal
// NOTE: Could easily loopify this...
unsigned long i_fract = 0;
if(b_fract & 0x80) i_fract += 50000000;
if(b_fract & 0x40) i_fract += 25000000;
if(b_fract & 0x20) i_fract += 12500000;
if(b_fract & 0x10) i_fract += 6250000;
if(b_fract & 0x08) i_fract += 3125000;
if(b_fract & 0x04) i_fract += 1562500;
if(b_fract & 0x02) i_fract += 781250;
if(b_fract & 0x01) i_fract += 390625;

// convert to decimal string format 00.00000000 with optional leading '-'
// Note: Could loopify this but need to calculate the subtractor
// values. Could do that using integer division (expensive), or
// integer multiplication (also expensive).
// BUT, could use a (fast) lookup table for the subtractor values
// to avoid division.

// first do the integer part

// do the tens
strOut[ch_p] = '0';
while(i_whole >= 10){	// tens
strOut[ch_p]++;	// count by characters
i_whole -= 10;
}
ch_p++;	// next write spot

// do the ones
strOut[ch_p] = '0';
while(i_whole >= 1){
strOut[ch_p]++;
i_whole -= 1;
}
ch_p++;

strOut[ch_p] = '.';	// decimal point
ch_p++;

// now do the fractional part

// do the '10,000,000'
strOut[ch_p] = '0';
while(i_fract >= 10000000){
strOut[ch_p]++;
i_fract -= 10000000;
}
ch_p++;

// do the '1,000,000'
strOut[ch_p] = '0';
while(i_fract >= 1000000){
strOut[ch_p]++;
i_fract -= 1000000;
}
ch_p++;

// do the '100,000'
strOut[ch_p] = '0';
while(i_fract >= 100000){
strOut[ch_p]++;
i_fract -= 100000;
}
ch_p++;

// do the '10,000'
strOut[ch_p] = '0';
while(i_fract >= 10000){
strOut[ch_p]++;
i_fract -= 10000;
}
ch_p++;

// do the 'thousands'
strOut[ch_p] = '0';
while(i_fract >= 1000){
strOut[ch_p]++;
i_fract -= 1000;
}
ch_p++;

// do the 'hundreds'
strOut[ch_p] = '0';
while(i_fract >= 100){
strOut[ch_p]++;
i_fract -= 100;
}
ch_p++;

// do the 'tens'
strOut[ch_p] = '0';
while(i_fract >= 10){
strOut[ch_p]++;
i_fract -= 10;
}
ch_p++;

// do the 'ones'
strOut[ch_p] = '0';
while(i_fract >= 1){
strOut[ch_p]++;
i_fract -= 1;
}
ch_p++;

strOut[ch_p] = 0;	// null terminator
}

void print_all_in_range() {
unsigned char byte;
char output[40];

for (int i = 0; i <= 255; ++i) {
byte = i;
software_ftoa(i, output);
printf("%s", output);
if (i != 255) printf(", ");
}
}

void print8bits (unsigned char buffer) {
for (unsigned char mask = 0x80; mask; mask >>= 1) {
if (mask & buffer) printf("1");
else printf("0");
}
printf("\n");
}

void print16bits (unsigned short buffer) {
for (unsigned short mask = 0x8000; mask; mask >>= 1) {
if (mask & buffer) printf("1");
else printf("0");
}
printf("\n");
}

void print32bits (unsigned long buffer) {
for (unsigned long mask = 0x800000; mask; mask >>= 1) {
if (mask & buffer) printf("1");
else printf("0");
}
printf("\n");
}

unsigned char software_float_add(unsigned char float1, unsigned char float2) {
unsigned short buffer1;
unsigned short buffer2;
unsigned short sum_buffer;
int exponent;
bool is_negative_float1 = false;
bool is_negative_float2 = false;
bool is_negative_sum = false;

if (float1 & 0x80) is_negative_float1 = true;
if (float2 & 0x80) is_negative_float2 = true;

exponent = (float1 & 0x07) - 4;
float1 &= 0x78;
float1 |= 0x80;

buffer1 = float1;
buffer1 <<= 8;
buffer1 >>= (7 - exponent);

exponent = (float2 & 0x07) - 4;
float2 &= 0x78;
float2 |= 0x80;

buffer2 = float2;
buffer2 <<= 8;
buffer2 >>= (7 - exponent);

// Maybe I'm totally missing something here, but I belive the addition of
// some logic to deal with negative addends is required for this to
// function properly.
if (is_negative_float1 || is_negative_float2) {

if (is_negative_float1 && is_negative_float2) {
is_negative_sum = true;
sum_buffer = buffer1 + buffer2;
}

else if (buffer1 >= buffer2) {
sum_buffer = buffer1 - buffer2;
if (is_negative_float1) is_negative_sum = true;
}

else {
sum_buffer = buffer2 - buffer1;
if (is_negative_float2) is_negative_sum = true;
}

}

else sum_buffer = buffer1 + buffer2;

printf("#1 Expanded: ");
print16bits(buffer1);
printf("#2 Expanded: ");
print16bits(buffer2);
printf("Sum: ");
print16bits(sum_buffer);

exponent = 7;
unsigned short bitfinder_mask = 0x8000;
while (!(sum_buffer & bitfinder_mask)) {
--exponent;
bitfinder_mask >>= 1;
}

if (exponent > 3 || exponent < -4) {
printf("Exponent of sum not within valid bounds.");
exit(0);
}

unsigned char the_float;

sum_buffer <<= (7 - exponent);
sum_buffer >>= 8;
printf("Sum Normalized: ");
print16bits(sum_buffer);
the_float = sum_buffer;
the_float &= 0x78;
exponent += 4;
the_float |= exponent;
if (is_negative_sum) the_float |= 0x80;
printf("Sum Packed: ");
print8bits(the_float);

return the_float;
}

unsigned char software_float_multiply(unsigned char, unsigned char) {
//TODO
return 0x00;
}

int software_float_pow(int base, int exponent) {
int x = 1;
for (int i = 0; i < exponent; ++i) {
x *= base;
}

return x;
}